## Slide 1: A framework for evaluating pavement vulnerability to shallow groundwater rise in coastal Alabama
Authors: Bruno J. de O. Sousa1,
Daniel B. Wright2, Bret M. Webb3, José G. Vasconcelos1
Presenter: Bruno Sousa
1Department of Civil and Environmental Engineering, Auburn University, Auburn, Alabama.
2Department of Civil and Environmental Engineering, University of Wisconsin-Madison
3Department of Civil, Coastal, & Environmental Engineering, University of South Alabama
2024 National Hydraulic Engineering Conference
Biloxi, Mississippi – Aug 29, 2024

## Slide 2: Context
Study area: Alabama State Route 180.
  Mobile Bay to the north, Gulf of Mexico to the south.
Vulnerability to flooding and high water tables.
Part of an effort to apply Nature-based solutions to improve coastal roadway resiliency
Notes: AL-180 serves as an evacuation route connecting Fort Morgan Peninsula to Dolphin Island.

## Slide 3: Context
Surface flooding.
High water tables may impact pavements*:
Complex groundwater evaluations.
Surface depression and holes.
Disintegration.
Increase compressive strain.
*Chen & Wang (2023); Titus-Glover et al. (2019)

## Slide 4: Objectives
This research intends to produce an intuitive framework to evaluate the exposure of AL-180’s pavement to elevated shallow groundwater levels (SGWL).
The framework is based on accumulated rainfall, proximity to water bodies, tidal level fluctuations, drawdown characteristics, and nearby roadway drainage.
Notes: AL-180 serves as an evacuation route connecting Fort Morgan Peninsula to Dolphin Island.

## Slide 5: Study Area Characteristics
Main Land Cover Classes: Open Water, Woody Wetlands, Emergent Herbaceous Wetlands, Developed, Low and Medium Intensity, Barren Land (Sand).
Predominant Soil: Sand.
Mean Annual Rainfall: 1581 mm (62 inches).
No streams in the peninsula
Notes: 100-meter buffer to include additional visible features in aerial images.

## Slide 6: Methods: Monitoring
3 groundwater monitoring wells
15 min Groundwater levels
HOBO water level loggers

## Slide 7: Methods – Study Delineation

## Slide 8: Methods – Groundwater Level Estimator

## Slide 9: Methods – Calibration
Static Water Level
Tidal amplitude effect

## Slide 10: Methods – Calibration
Groundwater level rise
Rainfall response

## Slide 11: Methods – Calibration
Drawdown as an exponential function.

## Slide 12: Methods : Calculation steps
Notes: Tem o original?

## Slide 13: Results – Groundwater Response

## Slide 14: Results – Calibration (The Pines)

## Slide 15: Results – Calibration (Boat Launch)

## Slide 16: Results – Validation (Navy Cove)

## Slide 17: Results – Validation (Navy Cove)

## Slide 18: Results – Evaluation
 | RMSE (m) | NSE
The Pines | 0.07 | 0.76
Boat Launch | 0.12 | 0.69
 | 0.1* | 0.75*
Navy Cove | 0.1 | 0.5
*Without the effect of the drainage channel.

## Slide 19: Results – GWL Exceedance Probability (Navy Cove)

## Slide 20: Results – Pavement Saturation (Navy Cove)
NOW
SLR (0.4 m*)
*0.4 m of sea level rise, which is equivalent to NOAA’s Intermediate High in 2050 or Low in 2100
GW table

## Slide 21: Future Research Direction
Hydraulic Conductivity
Evapotranspiration
AL-180 groundwater resilience index
Improve Static Level
Expand results

## Slide 22: Acknowledgments
Effects of Sea Level Rise (ESLR) program - National Oceanic and Atmospheric Administration (NOAA)
Federal Highway Administration (FHWA)
Alabama Department of Transportation (ALDOT)

## Slide 23: References
Chen, X., & Wang, H. (2023). Transportation Geotechnics Impact of sea level rise on asphalt pavement responses considering seasonal groundwater and moisture gradient in subgrade. Transportation Geotechnics, 40(April), 100992. https://doi.org/10.1016/j.trgeo.2023.100992
Titus-Glover, L., Darter, M. I., & Von Quintus, H. (2019). Impact of Environmental Factors on Pavement Performance in the Absence of Heavy Loads (Issue March).