## Slide 1
Hydrologic Modeling in SRH and SMS
August 29, 2024
2024 National Hydraulic Engineering Conference
Notes: This presentation will highlight new functionality that is currently being tested in the SRH / SMS platform for hydrologic simulation.

## Slide 2: Outline
Hydrologic Modeling
  General
  In SRH
    SRH-W, SRH-ONE, SRH-2D ?
    Unstructured
  In SMS
    Data Services
    Mesh Generation
    Dataset Creation
    Model Interface
Example Workflow

## Slide 3: Hydrologic Modeling
Basin Scale – Watershed
  “Inflows” from rain, snow melt, groundwater
  Generally, much larger scale than hydraulics
Transient (Varying time scale)
  Event based
  Long-term
Many parameters
  Meteorology (rain, wind, solar, …)
  Geology (soil, stratigraphy, water table, …)
  Land use (vegetation, permeability, …)
  Many uncertainties (+/- 30% ???)
Notes: Notes:
Generally, much larger scale
  Usually means lower resolution or very expensive computation
Transient – event based or long term
  Event based requires extensive “initial” or “antecedent” conditions
Parameters…

## Slide 4: Hydrology in SRH
SRH-2D History
  Flexible – use UGrid
Unstructured grid
  Cells should follow streams
Cell based datasets
  Bedrock elevation
  Sat/Unsat thicknesses
  Temperature
Rainfall
  Gage based
Notes: Like SRH-2D hydraulics, the hydrology is not on a regular grid.
Recommendation is to us an SMS UGrid
Cell based datasets
Most datasets in SMS / SRH-2D have historically been point based
SRH-2D computes values at the cells but they have been interpolated to the nodes for intuitive visualization
SRH-2D has used a cell-based approach for
Material type
Ceiling elevation
For hydrology in SRH, additional cell-based datasets are used.
Working model for internal projects.
Release to public anticipated.

## Slide 5: Hydrology Tools New in SMS
Data Acquisition
Mesh vs UGrid
  Datasets
  Conformity
Generation
  Unstructured feature based
Toolbox
  Python based tools (individual functionality)
  Watershed Delineation – (Watershed from Raster)
  Stream networks to channels – (Polygons from Arcs)
  UGrid generation – (UGrid from Coverage)
Notes: Specific tool name included in parenthesis

## Slide 6: Download from Web / Online Data Links
Download – Retrieve data for specified region and load into SMS
Online – Maintain link to web service and update with view
Notes: SMS includes features to download data for a selected region from web service sources or link to web service (dynamic maps).
Two commands in the “File” menu
Tools connected to the “Import from Web” macro (screen bounds or drag a box) and “Add Online” macro
Support for a single tile service
Support for a few feature services
Support for multiple map (image) services
  Seamless map sources that load images from the service using current screen area in the display projection.
  Can be converted to a static image.

## Slide 7: Available Data Sources
Terrain
  USGS 3DEP Bare Earth DEM
  Worldwide Elevation Data
  Others (Open Topography, CUDEM, SRTM15+)
Land Use
  NLCD 2011, 2006 (2021 now available)
  C-CAP (CONUS and Hawaii)
Soil Type
  Statsgo (state files)
  Ssurgo (county files)
  Global Land Cover
  Harmonized World Soil Database v 1.2
Notes: SMS includes specific connections to some web services
The interface allows user to configure connection to other services which follow protocols
Source Resolution Coverage
Terrain
USGS 3DEP Bare Earth DEM 1 m CONUS land
World Wide Elevation Data 3.7 m max world wide land
Open Topography pt data variable includes access to many other sources (SRTM15+, GEBCO,
CUDEM 3.4 m (1/9 arc second) partial
Land Cover
NLCD 30 m CONUS land
C-CAP 1-5 m CONUS and Hawaii
Soil type
Statago Vector polygons CONUS
Ssyrgi Vector polygons CONUS

## Slide 8: “Advanced…” Sources
User can associate additional web services with SMS
  Duplicate and modify existing web service
  Add link to new web service
  Add services view csv file
Add to the “defaults” list
Notes: Sources require:
Name – Usually user selected
Category (WMS, WFS, TMS) – Subtype required for WMS
URL
Layer (based on service). This can be queried in the dialog
Cell size limits
File abbreviation (for download)
Format
Can be flagged to appear on the main page as a “default” service in SMS

## Slide 9: 2D Mesh vs UGrid
Datasets
  2D Mesh supports only “node” based
  UGrid supports “node” and “cell” based
Conformity
  2D Mesh supports triangles and quadrilaterals
  UGrid supports all polygonal cells
    Voronoi
    Refinements (i.e. Quad tree)
    Can be constrained to limit cell types in a specific grid
Notes: Add pictures

## Slide 10: 2D Mesh or UGrid Generation – Best Practices
Minimize digitization and manual editing
  Feature extraction
    Streams
    Ridges
  Structures
    Bridges
    Culverts
Notes: Do we want to keep this slide?

## Slide 11: Toolbox
Python based tools
  Each tool is a library
Standard layout
  Includes help pane
History
Notes: The development of SMS continues to evolve. Current methodology emphasizes compartmentalization of functionality in Python libraries. This is illustrated in a new “Toolbox” available in SMS 13.2.
Engine specific interface tools are also being added.
This presentation will highlight many of these tools. Rather than simply summarize the tools, they will be presented via a workflow to create unstructured meshes for SRH-2D simulations.
The toolbox is divided into groups (folders) and includes a history option. When each tool is launched an interface dialog appears with associated help/instructions. More complex tools may have custom interfaces.

## Slide 12: Toolbox History Function
Re-run tools
Saved with project
Searchable
Editable
Input/Output

## Slide 13: Watershed Delineation
Input
  DEM
  Outlet Point
  Workflow Options
    Currently 2
  Accumulation threshold

## Slide 14: Stream Networks to Channel Polygons
Channel patches
  # of cells across
  Size and bias
  Auto-redistribution
Confluences / Intersections
Merge with basin
Notes: Confluences or intersections can result in odd shaped polygons, but it is handled in an generally acceptable way.
Clean up of resulting coverage available

## Slide 15: Resulting Grid / Mesh
Mesh Generation
  Domain field
  Flood plains / Basin
  “Auto patch”
Mesh Characteristics
  Matches features
  Minimal interaction
  May require manual cleanup
    Not necessarily a bad thing
Notes: Mesh steps
Assign all polygons at once
  Elevation source
  Patching
    Auto-detects
      Which polygons are valid patches
      Which nodes in polygon are “corners” or “split”
Select “Basin” polygons
  Not patches or manual
  Constant paving (background resolution specified)
Create “2D Mesh from Coverage”
  New python version
    Faster
    Higher quality cells/elements

## Slide 16: Dataset Calculator
Any Geometry
  Mesh, UGrid, Scatter, …
Cell or Node
Expression
Saved in history
“where” operator
  Min / Max
  Conditional / If
Notes: Examples and capabilities documented in the wiki, which is available as part of the tool

## Slide 17: Dataset from Interpolation
Surveys (TINs)
Gages
Boreholes

## Slide 18: Coverages / Layers
Rainfall stations
Exit location
Monitor / Gages

## Slide 19: Model Parameters
Simulation based
Like SRH-2D
  Intuitive
  Familiar

## Slide 20: Output
Hydrographs
  Stations
  Output
Water levels
Notes: Add a hydrograph

## Slide 21: FHWA Hydologic Modeling User’s Forum
Please join
Public.govdelivery.com/accounts/USDOTFHWA/subscriber/new?topic_id=USDOTFHWA_213

## Slide 22: Conclusion
Features available currently in SMS
  Can be applied to hydraulic models
Engine (SRH-2D) applied internally
Questions…
Megan Frye – megan.frye@dot.gov
Alan Zundel - azundel@aquaveo.com

## Slide 23: Conclusion
Thank you!
Questions?
Demo?
Alan Zundel
  azundel@aquaveo.com