## Slide 1: CA ERFO NP DEVA 2022-1(2) Salt Creek Interpretive Trail
Amanda Peters, CFLHD Hydraulic Engineer
*Unless otherwise noted, FHWA is the source of all images in this presentation

## Slide 2: CFL and ERFO Program
CFL: Central Federal Lands
Main Funding Source: ERFO Program
  Emergency Relief for Federally Owned Roads
  Intent: Restore facilities to pre-disaster condition

## Slide 3: Project Location
Source: https://www.nps.gov/deva/planyourvisit/maps.htm
Salt Creek Interpretive Trail

## Slide 4: Project Location
Source: https://www.nps.gov/deva/planyourvisit/maps.htm

## Slide 5: Project Significance
Source: https://www.nps.gov/deva/learn/nature/fish.htm
Salt Creek Pupfish
~1.5 in long
Provide educational opportunities while protecting sensitive habitat

## Slide 6: Pre-Disaster Conditions
Source: https://www.nps.gov/places/salt-creek.htm

## Slide 7: Disaster Events
August 2022: Flash Flooding
  Single Day Rainfall: 1.7 in
August 2023: Tropical Storm Hilary
  Single Day Rainfall: 2.2 in
Average Annual Rainfall in DEVA: 2 in
Significant damage throughout DEVA

## Slide 8: Post-Disaster Conditions

## Slide 9: Salt Creek Drainage Basin
Approximately 1500 sqmi. drainage basin
Outfall: Badwater Basin
Source: Google Earth
Annual Exceedance Probability (%) | Return Period (Year) | Computed Flow (cfs)
50 | 2 | 20
20 | 5 | 100
10 | 10 | 240
4 | 25 | 630
2 | 50 | 1,180
1 | 100 | 2,110
0.5 | 200 | 3,620
0.2 | 500 | 7,040

## Slide 10: Former Boardwalk
Originally Built: 1976
Most Recent Boardwalk Built: 1997
Cast in Place Concrete Piers
Douglas Fir Decking
Source: NPS

## Slide 11: Project Constraints

## Slide 12: Design Approach & Criteria
Hydraulic Capacity Design Event: 25 yr (no pressure flow)
Scour Design Event: 50 yr
Scour Check Event: 100 yr

## Slide 13: Boardwalk Capacity Design
Ensure the boardwalk is not under pressure flow for the 25 yr event
SMS Version 13.2.17
SRH-2D: Flow and Sediment
Flow

## Slide 14: Sediment Transport – Model Development
Sandy Streambed Material
Wide floodplain and zone of sediment movement

## Slide 15: Topographic Comparison
October 2022
October 2023

## Slide 16: Sediment Transport Comparison
LiDAR Comparison: 2022-2023
Pre-Tropical Storm Hilary Sediment Transport Results (100 yr)
Flow
Flow

## Slide 17: Post-Hilary Sediment Transport
Post-Tropical Storm Hilary Sediment Transport Results (100 yr)
Flow

## Slide 18: Scour Zones
Scour Zone 1
Scour Zone 2
Scour Zone 3
Scour Zone 4
Scour Zone 5
Scour Zone 6
Scour Zones 1, 2, 3 & 4: 5-” Helical Pile
Scour Zone 5: 7” Helical Pile
Scour Zone 6: 2-” Helical Pile

## Slide 19: Helical Pile Scour
HEC-18 Pier Scour Equation (non-standard approach)
Scour Design Event: 1.2 x single helical pile scour depth
Scour Check Event: Debris considerations (wall pier)

## Slide 20: Scour Results
Hydraulic Data |  |  |  | 
Scour Zone | 50-yr Storm Total Scour (Ft) | 50-yr Maximum Velocity (fps) | 100-yr Storm Total Scour (Ft) | 100-yr Maximum Velocity (fps)
1 | 6.0 | 6.7 | 7.0 | 7.9
2 | 5.5 | 4.3 | 7.0 | 5.4
3 | 5.5 | 10.0 | 7.5 | 12.3
4 | 6.0 | 4.6 | 7.0 | 5.8
5 | 5.5 | 7.1 | 7.0 | 7.9
6 | 1.0 | 1.0 | 1.5 | 6.5
Combination of sediment transport model results and local (pier) scour

## Slide 21: Existing Boardwalk Removal

## Slide 22: Salt Creek Road
Road and parking area raised to avoid inundation by 25 year event
Embankment Protection

## Slide 23: Conclusion
SRH-2D used for hydraulic modeling and sediment transport
Proposed Boardwalk: Helical piles with Douglas Fir decking
Anticipated Construction Start: December 2024
Anticipated Construction Completion: May 2025

## Slide 24: Questions?