## Slide 1: Watershed Surface and Channel Runoff Coefficient Assessment with Unified Runoff Time Implications
Ken Kagy P.E., CFM, CPSWQ, CPESC
AN EVALUATION OF ESTIMATING the TIME of CONCENTRATION to DETERMINE PEAK RUNOFF FLOWS for SMALL WATERSHED BASINS
2024 National Hydraulic Engineering Conference
Notes: Intro Slide
Top: Add Presentation Title, Bottom: Add Presenter Name(s) (Name, Affiliation)

## Slide 2
Taken from Wanielista, M., R. Kersten, and R. Eaglin, Hydrology: Water Quantity and Quality Control, p. 184
SCS Method
Time of Concentration’s Definition
  Time of Concentration tc: Time required for water to travel from the most hydraulically remote point in the basin to the basin outlet.
This time is determined by drainage characteristics such as surface density, slope, channel roughness, and soil infiltration. Many empirical equations have been developed through watershed research.

## Slide 3: Sheet Flow
Precipitation
Sheet Flow
Sheet flow
Infiltration
A basin unit flow expressed by an implicit channelized flow
(Used in surface & channel flow)
Manning’s Kinematic Wave Eq.
TR-55 Sheet Flow—The sheet flow time computed for each area of sheet flow that requires the following input data:
Hydraulic Length—Defined flow length for the sheet flow.
  Manning's n—Manning's roughness value of the sheet flow.
  Slope— The defined slope of the sheet flow/catchment.

## Slide 5: Sheet Flow Limitations National Engineering Handbook
Kibler and Aron (1982) and others indicated the maximum sheet flow length is less than 100 feet. To support the sheet flow limit of 100 feet, Merkel (2001) reviewed a number of technical papers on sheet flow. McCuen and Spiess (1995) indicated larger sheet flow length variables lead to less accurate designs, and proposed a limitation with equation (15–8) shown below be considered:
Eq. 15-8
where:
n = Manning’s roughness coefficient
l = limiting length of flow (ft)
S = slope (ft/ft)

## Slide 6: What are ‘n’ Sheet Flow Relationships to Other Surface Runoff Values?
Percent Impervious | Manning’s Low ‘n’ Sheet Flow Values | Manning’s High ‘n’ Sheet Flow Values | Manning’s Average ‘n’ Sheet Flow Values
1% | 0.700 | 0.800 | 0.750
 | 0.450 | 0.550 | 0.500
30% | 0.300 | 0.480 | 0.390
 | 0.160 | 0.420 | 0.290
 | 0.100 | 0.200 | 0.150
 | 0.022 | 0.033 | 0.028
99% | 0.011 | 0.015 | 0.013

## Slide 7: Sheet Flow ‘n’ Coefficient Interpolated to Percent Impervious Surface
Percent Impervious | Exponential ‘n’ Values | Linear ‘n’ Values | Polynomial ‘n’ Values | Average ‘n’ Sheet Flow Values
1% | 0.750 | 0.750 | 0.750 | 0.750
10% | 0.650 | 0.623 | 0.625 | 0.633
20% | 0.424 | 0.551 | 0.501 | 0.492
30% | 0.276 | 0.480 | 0.390 | 0.382
40% | 0.180 | 0.408 | 0.293 | 0.294
50% | 0.117 | 0.337 | 0.211 | 0.222
60% | 0.076 | 0.265 | 0.143 | 0.162
70% | 0.050 | 0.194 | 0.089 | 0.111
80% | 0.032 | 0.122 | 0.049 | 0.068
90% | 0.021 | 0.051 | 0.024 | 0.032
99% | 0.013 | 0.013 | 0.013 | 0.013

## Slide 8: Shallow Concentrated Flow
NRCS definition of shallow flow is 1 inch to 6 inches deep
Chapter 15 Part 630 of National Engineering Handbook
Channelized Flow Time

## Slide 9: Shallow Flow Equations from NEH, May 2010

## Slide 10: Shallow Flow Velocity Equations for 0.25 ft. of Depth and Manning's “n”
Mannings “n” Value | Depth of Flow (ft.) | Velocity Equations (ft./s)
0.200 | 0.25 | V = 2.949(s)0.5
0.160 | 0.25 | V = 3.686(s)0.5
0.130 | 0.25 | V = 4.536(s)0.5
0.110 | 0.25 | V = 5.361(s)0.5
0.086 | 0.25 | V = 6.857(s)0.5
0.067 | 0.25 | V = 8.802(s)0.5
0.052 | 0.25 | V = 11.341(s)0.5
0.039 | 0.25 | V = 15.121(s)0.5
0.029 | 0.25 | V = 20.335(s)0.5
0.022 | 0.25 | V = 26.805(s)0.5
0.013 | 0.25 | V = 45.363(s)0.5

## Slide 11: Open Channel Flow Equation
Tc conveyance flow = Length / Velocity
Manning’s Equation
Hydraulic Radius Can Equal Flow Depth in Manning’s Eq. for Small-Wide Channels
NRCS’s considers 6 in. or deeper to be channel flow
An initial 8 in. depth is used to initiate channel flows
& increased to 16 in. depth for an average depth of 1 ft.
Conveyance Flow for Uniform Geometry

## Slide 12: Manning’s ‘n’ Channel Coefficients
From USACE, January 2010, HEC-RAS River Analysis System, Hydraulic Reference Manual, Version 4.1.

## Slide 13: Velocity Equations with an 8 to 16 Inch Flow Depth for a Channel “n” Value
Mannings “n” Value | Initial Depth of Flow (ft.) | Velocity Equations (ft./s) | Ending Depth of Flow (ft.) | Velocity Equations (ft./s)
0.140 | 0.67 | V = 8.127(s)0.5 | 1.35 | V = 13.157(s)0.5
0.120 | 0.67 | V = 9.482(s)0.5 | 1.35 | V = 15.349(s)0.5
0.100 | 0.67 | V = 11.378(s)0.5 | 1.35 | V = 18.419(s)0.5
0.085 | 0.67 | V = 13.386(s)0.5 | 1.35 | V = 21.670(s)0.5
0.074 | 0.67 | V = 15.376(s)0.5 | 1.35 | V = 24.891(s)0.5
0.057 | 0.67 | V = 19.962(s)0.5 | 1.35 | V = 32.314(s)0.5
0.042 | 0.67 | V = 27.091(s)0.5 | 1.35 | V = 43.855(s)0.5
0.034 | 0.67 | V = 33.465(s)0.5 | 1.35 | V = 54.174(s)0.5
0.027 | 0.67 | V = 42.141(s)0.5 | 1.35 | V = 68.219(s)0.5
0.021 | 0.67 | V = 54.181(s)0.5 | 1.35 | V = 87.711(s)0.5
0.012 | 0.67 | V = 94.817(s)0.5 | 1.35 | V = 153.494(s)0.5

## Slide 14: Visualizing Tc with Manning’s ‘n’, McCuren & Spiess Limits, & NRCS Velocity Equations
Sheet flow lengths are 90-110 ft. for 2 & 10% slopes respectively at a full impervious surface
Shallow concentrated flow lengths are 400-500 ft. for 2 & 10% slopes respectively at a full impervious surface
The remaining flow path length is considered channel flow with a comparable Manning’s ‘n’ coefficient to the sheet flow and shallow flow.
The Following Plot is Tc Velocity Eq. Boundary:
Sheet Flow Tt = 0.007(nL)0.8/(P20.5S0.4)
Shallow Concentrated Flow Tt = L /3600V
Open Channel Flow Tt= (L*n) /(1.49R0.67S 0.5)
(Manning’s Equation)
  Where Hydraulic Radius = conveyance flow depth then:
  Manning’s equation becomes Tt = L/3600V
Total Watershed Time of Concentration
tc=STt
  L= ft., Tt = hr., S= % slope, R= ft., P= in.(2yr.24hr.) , V= ft./sec.

## Slide 15
Tc Pervious & Impervious Boundaries for 1% & 12% Basin slopes Respectively
@ 1% Slope
@ 12% Slope
Most Tc occurs in this Area

## Slide 16: NRCS’s ‘CN’ Values for Soil Groups

## Slide 17: Percent Impervious Surface to the Soil Group’s Average ‘CN’ Value
Percent Impervious | Soil Group A | Soil Group B | Soil Group C | Soil Group D | Average ‘CN’ Value for All
1% | 30 | 55 | 70 | 77 | 58.00
12% | 46 | 65 | 77 | 82 | 67.50
20% | 51 | 68 | 79 | 84 | 70.50
25% | 54 | 70 | 80 | 85 | 72.25
30% | 57 | 72 | 81 | 86 | 74.00
38% | 61 | 75 | 83 | 87 | 76.50
65% | 77 | 85 | 90 | 92 | 86.00
72% | 81 | 88 | 91 | 93 | 88.25
85% | 89 | 92 | 94 | 95 | 92.50
99% | 98 | 98 | 98 | 98 | 98.00

## Slide 18: Rational ‘C’ Coefficient with Soil Types

## Slide 19: Percent Impervious Surface to the Soil Group’s Average ‘C’ Value
Percent Impervious | Soil Group A | Soil Group B | Soil Group C | Soil Group D | Average ‘C’ Value for All
1% | 0.095 | 0.125 | 0.145 | 0.180 | 0.137
12% | 0.208 | 0.235 | 0.277 | 0.320 | 0.260
20% | 0.225 | 0.245 | 0.285 | 0.320 | 0.269
25% | 0.245 | 0.275 | 0.310 | 0.340 | 0.293
30% | 0.275 | 0.305 | 0.335 | 0.360 | 0.319
38% | 0.300 | 0.330 | 0.355 | 0.380 | 0.341
65% | 0.370 | 0.400 | 0.420 | 0.450 | 0.410
72% | 0.765 | 0.770 | 0.775 | 0.775 | 0.771
85% | 0.795 | 0.805 | 0.805 | 0.805 | 0.803
99% | 0.910 | 0.910 | 0.910 | 0.910 | 0.910

## Slide 20: 10% Impervious Surface Increments Normalized to ‘CN’ & ‘C’ Coefficients
These Values are Plotted in the Following Graphs:
Percent Impervious | Average ‘n’ Sheet Flow Coefficients | Calculated Average ‘CN’ Value from % | Calculated Average ‘C’ Value from %
1% | 0.750 | 58.0 | 0.14
10% | 0.655 | 63.5 | 0.19
20% | 0.511 | 68.1 | 0.25
30% | 0.395 | 72.6 | 0.31
40% | 0.302 | 76.8 | 0.38
50% | 0.225 | 80.8 | 0.46
60% | 0.161 | 84.6 | 0.54
70% | 0.106 | 88.3 | 0.63
80% | 0.060 | 91.7 | 0.72
90% | 0.021 | 94.9 | 0.82
99% | 0.013 | 98.0 | 0.91

## Slide 21: Flow Path vs. Tc for 2% slope path

## Slide 22: Flow Path vs. Tc for 5% slope path

## Slide 23: Flow Path vs. Tc for 10% slope path

## Slide 24: Kirpich Tc Equation
      Tc
      A Tc equation modeled from channelized basins
Tc = minutes, Lc = flow path length (ft.)
Sc = flow path slope in (ft./ft.)
Kirpich is an accepted method in estimating Tc on small basins (1 - 112 acres). It was developed from 7 rural watersheds with basin slopes (3 to 10%) for an assumed bare soil flow paths.
The slope Sc is the elevation difference between the most remote point to the outlet divided by the flow path length Lc.

## Slide 25: Comparisons of Kirpich Equation Factors to other Runoff Coefficients
Ground Cover | Kirpich Adjustment Factor, ‘k’ (Chow, 1988; Chin, 2000)
General overland flow and natural grass channels | 2.0
Overland flow on bare soil or roadside ditches | 1.0
Overland flow on concrete or asphalt surfaces | 0.4
Flow in concrete channels | 0.2

## Slide 26: Extrapolated ‘k’ Factor for Maximum Projected 2.9 ‘k’ & minimum 0.35 ‘k’
Basin’s Percent Impervious | Kirpich ‘k’ Adjustment factor
1% | 2.93
10% | 2.58
20% | 2.21
30% | 1.88
40% | 1.57
50% | 1.30
60% | 1.04
70% | 0.82
80% | 0.63
90% | 0.46
99% | 0.34

## Slide 27: Average ‘CN’, ‘C’, ‘k’, & ‘n’ Coefficients Normalized to 10% Impervious Surface
Percent Impervious | Calculated ‘CN’ Values from % | Calculated ‘C’ Values from % | Kirpich ‘k’ Values from % | ‘n’ Sheet Flow Coefficients
1% | 58.0 | 0.14 | 2.93 | 0.750
10% | 63.5 | 0.19 | 2.58 | 0.655
20% | 68.1 | 0.25 | 2.21 | 0.511
30% | 72.6 | 0.31 | 1.88 | 0.395
40% | 76.8 | 0.38 | 1.57 | 0.302
50% | 80.8 | 0.46 | 1.30 | 0.225
60% | 84.6 | 0.54 | 1.04 | 0.161
70% | 88.3 | 0.63 | 0.82 | 0.106
80% | 91.7 | 0.72 | 0.63 | 0.060
90% | 94.9 | 0.82 | 0.46 | 0.021
99% | 98.0 | 0.91 | 0.34 | 0.013

## Slide 28: Kirpich & Velocity Eq. Tc’s Compared

## Slide 29: Kirpich & Velocity Eq. Tc’s Compared

## Slide 30: Kirpich & Velocity Eq. Tc’s Compared

## Slide 31: NRCS’s LAG Equation
      Tlag
      Tc
      A Tc equation formed with the basin’s surface data
Tlag= Lag time (hrs.), Lc = flow path length (ft.)
Yc = average watershed slope number percent (%)
Tc= Time of Concentration (minutes) IF & CF = FHWA Adjust. Factors
NRCS lag method was developed by Mockus in 1961 for many conditions from heavy forest, meadows, and paved areas less than 2000 acres. Referenced by NRCS as a TC.

## Slide 32: NRCS Lag & Velocity Tc’s Compared

## Slide 33: FHWA (HEC19) Adjustment Factors for NRCS Lag Eq. on imperviousness & channel improvements
= NRCS’s adjustment factors on Lag Eq. for percent imperviousness and channel improvements
= the percent imperviousness or percent of main channels that are hydraulically improved beyond natural conditions.

## Slide 34: Lag Imp. & Channel Factors vs. Velocity

## Slide 35: Lag Imp. & Channel Factors vs. Velocity

## Slide 36: Lag Imp. & Channel Factors vs. Velocity

## Slide 37: FAA’s Tc Equation
      Tc
      A Tc equation formed with basin’s surface data
Tc = minutes, Lc = flow path length (ft.)
Sc = flow path slope in (% full number)
C = Rational Runoff Coefficient
Developed from airfield drainage with data assembled by USACE. It is frequently used on urban watersheds.
This equation was developed in an environment of primarily sheet & shallow flow, low slopes, higher impervious surfaces, and on small drainage basins.

## Slide 38: FAA Tc vs. Velocity Tc’s Compared
No Channelization Factor

## Slide 39: Small Watershed Runoff Response
Tc comparison graphs between the velocity equations and channelized empirical equations convey a systematic intersect for each related surface coefficient.
Empirical equations provide a lower Tc in short flow paths while velocity equations for a same flow path exhibits a higher Tc. Empirical equations calculate higher Tc’s on longer basin flow paths while velocity equations assess a reduced time for the same longer flow path.
Runoff time on small basins exhibits a transformation from a “surface” attribute flow dominance to a “channel” attribute flow dominance.
TOC - Timing Outside Channel TIC - Timing Inside Channel
Consider a predictable Tc equation for known observations of related Tc equations in multi-surfaced watersheds from recently acquired graphs.

## Slide 40
Combined for a 2% Slope Watershed
Dominated by
T O C
Dominated by
T I C

## Slide 41
Combined for a 10% Slope Watershed
Dominated by
T I C
Dominated by
T O C

## Slide 42: Unified Tc Equation with Channelization using % Impervious Surface
  Tc
Tc = Time of Concentration (minutes)
= Length of Flow Path (feet)
= % Impervious Surface (decimal format)
= % Slope of Flow Path (decimal format)
Equation Limits: 1 to 325 acres of drainage basin 1 to 12 percent slope of flow path 1 to 99 percent impervious surface

## Slide 43
UTC Eq. vs. Lag, Kirpich, & Velocity Curves

## Slide 44
UTC Eq. vs. Lag, Kirpich, & Velocity Curves

## Slide 45
UTC Eq. vs. Lag, Kirpich, & Velocity Curves

## Slide 46: Unified Tc Equation with Channelization using CN Values
  Tc
Tc = Time of Concentration (minutes)
= Length of Flow Path (feet)
= NRCS’s Average Runoff Curve Number
= % Slope of Flow Path (decimal format)
Equation Limits: 1 to 350 acres of drainage basin 1 to 15 percent slope for flow path 55 to 98 surface runoff curve number

## Slide 47
‘CN’ Avg. Relationships for Soil Types

## Slide 48: Unified Tc Equation uses an average CN Soil type (near B soil type)
Basin weighed CN value is attained by adjusting CN soil types to a CNavg type
  CNavg
CNavg = Average CN values used in Unified Tc Equation
= NRCS’s Runoff Curve Number per soil type
= NRCS’s soil type factor shown below
Type A Soil: x = 0 Type B Soil: x = 1
Type C Soil: x = 2 Type D Soil: x = 3

## Slide 49: Unified Tc Equation for Channelization using ‘C’
  Tc
Tc = Time of Concentration (minutes)
= Length of Flow Path (feet)
= Rational method’s average runoff coefficient
= % Slope of Flow Path (decimal format)
Equation Limits: 1 to 225 acres of drainage basin 1 to 12 percent slope for flow path 0.10 to 0.95 rational runoff coefficient

## Slide 50
‘C’ Avg. Relationships for Soil Types
using a 10yr. Storm Event

## Slide 51
Unified Tc Equation uses an average ‘C‘ coefficient (near B soil type)
Basin weighed ‘C’ value is attained by adjusting ‘C’ soil types to a ‘Cavg’ type
  Cavg
  Cavg = Average C values used in Unified Tc Equation
  = Rational method’s runoff coefficient per soil type
  = NRCS’s soil type factor shown below
  Type A Soil: x = 0 Type B Soil: x = 1
  Type C Soil: x = 2 Type D Soil: x = 3

## Slide 52: The Iowa Storm Water Management Manual

## Slide 53: UDFCD Runoff Coefficients

## Slide 54
Unified Tc C Equation with Pennsylvania’s local ‘C’ Value for a Local 10 yr. Event

## Slide 55
Unified Tc ‘C’ Equation with Iowa’s local ‘C’ values for a 10 yr. Event

## Slide 56
Unified Tc ‘C’ Equation with Colorado’s Local ‘C’ values for a Local 10 yr. Storm

## Slide 57
Kinematic Wave Theory is Significant in Prevailing Hydrology Flow Equations
Kinematic wave method relates flows to the basin characteristics.
Kinematic basin routing parameters define the channel shape, boundary roughness, and slope of the flow routing surface.
Flood runoff waves are defined by two studies of motion kinematic and dynamic (changes in discharge, velocity, & surface elevations) wave equations.
Kinematic wave equations govern flow with forces essentially from flow of fluid weight balanced by surface resistive forces.
Kinematic wave approximation is an accurate & efficient method of modeling storm water runoff for both overland flow & channel routing. (Overton & Meadows, 1976)

## Slide 58: Papadakis-Kazan Tc Equation
      A global regression equation derived from eleven Tc equations
Tc = minutes, L = flow path length (ft.)
n = Manning’s Coefficient, S = flow path slope in (ft./ft.)
i = Rainfall Intensity (in./hr.), k = Constant
Developed from frequent Tc equations that includes Kirpich, Izzard, Kerby/Hathaway, Carter, Eagleson, Kinematic Wave, Morgali, Linsley, FAA, SCS Velocity , SCS Curve (Lag), and Singh’s Kinematic Wave/Chezy equations.
Examination of existing equations used for time of concentration revealed a shared a general format. The resulting upper right equation right provides an general applicable Tc equation with a predetermined degree of confidence.
The common exponents a, b, y, z, and the constant k for the 4 variables were formed from 375 data points on natural and experimental watersheds of less than 500 acres. A regression analysis was performed for each with a best fit.

## Slide 59
Papadakis-Kazan Tc with Manning's Channel ‘n’ Value Compared to Velocity & UTC Equations
Percent Impervious | ‘n’ Sheet Coefficients | ‘n’ Shallow Coefficients | ‘n’ Channel Coefficients
1% | 0.750 | 0.200 | 0.140
10% | 0.655 | 0.160 | 0.120
20% | 0.511 | 0.130 | 0.100
30% | 0.395 | 0.110 | 0.085
40% | 0.302 | 0.086 | 0.074
50% | 0.225 | 0.067 | 0.057
60% | 0.161 | 0.052 | 0.042
70% | 0.106 | 0.039 | 0.034
80% | 0.060 | 0.029 | 0.027
90% | 0.021 | 0.022 | 0.021
99% | 0.013 | 0.013 | 0.012

## Slide 60
Papadakis-Kazan Tc with Manning’s Shallow ‘n’ Value Compared to Velocity & UTC Equations
Percent Impervious | ‘n’ Sheet Coefficients | ‘n’ Shallow Coefficients | ‘n’ Channel Coefficients
1% | 0.750 | 0.200 | 0.140
10% | 0.655 | 0.160 | 0.120
20% | 0.511 | 0.130 | 0.100
30% | 0.395 | 0.110 | 0.085
40% | 0.302 | 0.086 | 0.074
50% | 0.225 | 0.067 | 0.057
60% | 0.161 | 0.052 | 0.042
70% | 0.106 | 0.039 | 0.034
80% | 0.060 | 0.029 | 0.027
90% | 0.021 | 0.022 | 0.021
99% | 0.013 | 0.013 | 0.012

## Slide 61
Papadakis-Kazan Tc with Manning’s Sheet ‘n’ Value Compared to Velocity & UTC Equations
Percent Impervious | ‘n’ Sheet Coefficients | ‘n’ Shallow Coefficients | ‘n’ Channel Coefficients
1% | 0.750 | 0.200 | 0.140
10% | 0.655 | 0.160 | 0.120
20% | 0.511 | 0.130 | 0.100
30% | 0.395 | 0.110 | 0.085
40% | 0.302 | 0.086 | 0.074
50% | 0.225 | 0.067 | 0.057
60% | 0.161 | 0.052 | 0.042
70% | 0.106 | 0.039 | 0.034
80% | 0.060 | 0.029 | 0.027
90% | 0.021 | 0.022 | 0.021
99% | 0.013 | 0.013 | 0.012

## Slide 62
Mathematical Boundaries of Variables in the UTC, Kinematic Wave Flow, and Papadakis-Kazan Equations
Surface Boundary Coefficient’s have Hydrologic Value Limits by Hydrology Definitions. However, These Limits May Not Exist within a Mathematic Equation.
UTC Eq. plotted for Impervious Surface Boundary
UTC Eq. plotted Surface Boundary of NRCS CN Values

## Slide 63
Mathematical Boundaries of Variables in the UTC, Kinematic Wave Flow, and Papadakis-Kazan Equations
Surface Boundary Coefficient’s ‘n’ at the Vertical Axis can be Estimated with a Range of Limits for ‘s’ and ‘i’ for the Entire Limits of the Mathematic Equation.
Kinematic Equations plotted for Surface Boundary of Manning’s ‘n’ Value
Papadakis-Kazan Equation plotted for Surface Boundary of Manning’s ‘n’ Value

## Slide 64
An Evaluation of the Papadakis-Kazan Tc Equation for a Full Range of Manning's Sheet Flow ‘n’ Values
Papadakis-Kazan Equation Arranged for Rainfall Intensity
Partial Multi-Variable Derivative of Papadakis-Kazan Eq. with respect to ‘L’
Papadakis-Kazan
‘i’ Optimized for Manning’s Sheet Flow ‘n’ Values
=

## Slide 65
Papadakis-Kazan Tc Compared to Velocity & UTC Eqs.

## Slide 66
Papadakis-Kazan Tc Compared to Velocity & UTC Eqs.

## Slide 67
Papadakis-Kazan Tc Compared to Velocity & UTC Eqs.

## Slide 68
Papadakis-Kazan Tc Equation for Surface Boundary Conditions with Manning’s ‘n’ Sheet Flow Coefficients
Percent Impervious | ‘n’ Sheet Coefficients
1% | 0.750
10% | 0.655
20% | 0.511
30% | 0.395
40% | 0.302
50% | 0.225
60% | 0.161
70% | 0.106
80% | 0.060
90% | 0.021
99% | 0.013
Tc = Time of Concentration (minutes)
= Length of Flow Path (feet)
n = Manning’s Sheet Flow Coefficient
= % Slope of Flow Path (decimal format)
Equation Limits: 1 to 500 acres of drainage basin 1 to 12 percent slope for flow path 0.013 to 0.75 Manning’s sheet surface ‘n’ value
. Papadakis-Kazan with surface and channelization attributes

## Slide 69
The Complexities of a Tc Equation when Properly Applied to a Basin’s Attributes Can Reasonably Estimate a Response Time for Storm Water Runoff
Ken Kagy, P.E., CFM, CPSWQ, CPESC (770) 343-8365 kenkagy@yahoo.com
Time of Concentration is Vital to Hydrograph Peak Flow Assessment And a Reasonably Estimated Tc can Vary Peak Flows by 300%.
Understanding the required variables in a time of concentration equation.
Understanding the limits to each variable in a time of concentration equation.
Understanding a basin’s flow path with its flow type, length, depth, and slope.
Apply acceptable surface roughness Tc coefficients that correlate to equivalent hydrology’s surface roughness conditions used to calculate the hydrograph.
The Accuracy of Time Equations are Improved with the following: