## Slide 1
Taking on River Woes:
The Whitewater River Bridge’s Battle with Bed Degradation in California’s High Desert
NHEC 2024
Biloxi, Mississippi
Date: August 28, 2024
Presented by:
Oscar Suaznabar
2019
Notes: Good morning/afternoon everyone.
Today, I am excited to present to you our project on addressing scour and channel bed degradation at the Whitewater River Bridge located in the high desert region of Southern California.
This bridge, which plays a critical role in the local transportation network, has been facing significant challenges due to extensive scour and ongoing channel bed degradation, exacerbated by recent extreme weather events.
Our project aims to thoroughly investigate these issues using innovative surveying techniques,
and to develop effective mitigation strategies to enhance the bridge's resilience and ensure its long-term stability.

## Slide 2
Name of Structures: Whitewater River
Location: District 8 – Riverside County
Facility Carried: INTERSTATE 10
Upstream Bridge: Br.No. 56-0004L (I-10 WB)
Structure Length: 507.5 feet (8 Spans)
Lanes: 4
ADT: 39500 (Truck ADT 22%)
Downstream Bridge: Br.No. 56-0004R (I-10 EB)
Structure Length: 502.3 feet (8 Spans)
Lanes: 4
ADT: 39500 (Truck ADT 22%)
1. OVERVIEW

## Slide 3
2008, designated SCOUR CRITICAL, attributed to streambed degradation in the vicinity of the structure and the potential for undermining of the spread footings.
2008, Placement of rock slope protection (RSP) around Piers 6 and 7.
2013, RSP was installed around the two abutments and the remaining piers.
2. BRIEF HISTORY
Original Structure built in 1952, 8 Span continuous RC “T-beam” girder with RC deck on RC pier walls and diaphragm abutments. All on spread footings.
1967, Left and Right Widening.

## Slide 4
2021 – Scour
Mitigation Retrofit
As-Built Plans
Incorporating rock slope protection (RSP) on both abutment slopes that extended to the adjacent Piers 3 and 7, respectively.
Pile caps were retrofitted with the addition of 36-inch diameter Cast-In-Drilled-Hole (CIDH) piles at the foundation of Piers 3, 4, 5, 6, and 7.
2. BRIEF HISTORY CONT’D

## Slide 5
3. FIELD INVESTIGATION (2023-2024)
Historic rainfall in August 2023 – Tropical Storm Hilary
Rainfall totals from Hilary reached 11.7 inches in approx. 24 hours in the San Bernardino Mountains.
San Bernardino Mountains drain into Coachella Valley through Whitewater River.
Source: hpnonline.org
https://www.reddit.com/r/Damnthatsinteresting/comments/15wv7kg/massive_debris_flow_in_palm_springs_ca_from/?utm_source=share&utm_medium=mweb3x&utm_name=post_embed&utm_term=1&utm_content=1
Link to Video:

## Slide 6
3. FIELD INVESTIGATION
SEPTEMBER - OCTOBER 2023
From Upstream, looking downstream at Pier 5 of left bridge.
Pier 6
Pier 5
From Upstream, looking downstream at Pier 6 of left bridge.

## Slide 7
3. FIELD INVESTIGATION
FEBRUARY 2024
From Upstream, looking downstream at Pier 5 of left bridge.
Pier 6
Pier 5
From Upstream, looking downstream at Piers 5 and 6 of left bridge.
Pier 6
Pier 5
Pier 5

## Slide 8
From Downstream, looking upstream at Pier 5 of right bridge.
From Downstream, looking upstream at Pier 6 of right bridge.
Pier 6
Pier 5
3. FIELD INVESTIGATION
SEPTEMBER - OCTOBER 2023

## Slide 9
3. FIELD INVESTIGATION
FEBRUARY 2024
Pier 6
Pier 5
From Downstream, looking upstream at Pier 5 of right bridge.
Standing under Span 5, looking at
Pier 6 of right bridge.

## Slide 10
3. FIELD INVESTIGATION
FEBRUARY 2024
Pier 5
From Downstream, looking upstream at Pier 5 of right bridge.

## Slide 11
Skydio 3D Scan Mapping:
Drone plans a path based on AI-driven workflow.
Drone plans a path based on AI-driven workflow
Drone autonomously captures all surfaces of a scene.
3. FIELD INVESTIGATION (2023-2024)
METHODOLOGY AND TOOLS USED

## Slide 12
Drone plans a path based on AI-driven workflow
Drone autonomously captures all surfaces of a scene.
Conventional UAS-based Photogrammetry
+
Skydio 3D Scan Mapping:
Field Investigation October 2023
3. FIELD INVESTIGATION (2023-2024)
METHODOLOGY AND TOOLS USED

## Slide 13
Conventional UAS-based Photogrammetry
+
Skydio 3D Scan Mapping
Field Investigation October 2023
3. FIELD INVESTIGATION (2023-2024)
METHODOLOGY AND TOOLS USED

## Slide 14
3. FIELD INVESTIGATION
OCTOBER 2023 VS. FEBRUARY 2024
Pier 6
3D Point Cloud – October 2023 (Skydio 3D Scan)
3D Point Cloud – February 2024
(Skydio 3D Scan)
Pier 6
Pier 5
Pier 5

## Slide 15
3. FIELD INVESTIGATION
OCTOBER 2023 VS. FEBRUARY 2024 CONT’D
3D Point Cloud – October 2023
Pier 5
Pier 6
Average Bed Elevation
October 2023

## Slide 16
3D Point Cloud – February 2024
Pier 5
3. FIELD INVESTIGATION
OCTOBER 2023 VS. FEBRUARY 2024 CONT’D
Average Bed Elevation
October 2023
Pier 6
Average Bed Elevation
February 2024

## Slide 17
Elevation Contour Map February 2024 (Current Conditions)
Elevation Contour Map October 2023
Elevation Contour Map 2019 (Before Hilary)
4. HYDRAULIC AND SCOUR RE-EVALUATION

## Slide 18
October 2023
February 2024
2019
4. HYDRAULIC AND SCOUR RE-EVALUATION CONT’D
Bridge Location

## Slide 19
P6
P5
P6
P5
SRH-2D Simulation of Flood Conditions for Hurricane Hilary based on
2019 Bed Topography:
Estimated Peak Flow during Hilary: 24,000 CFS (50-yr Event)
Peak Velocities at the I-10 White Water River Bridge 12 – 14 [ft/s].
CRITICAL VELOCITY INDEX: CVI = Modeled Velocity / Critical Velocity
P6
P5
P6
P5
4. HYDRAULIC AND SCOUR RE-EVALUATION CONT’D

## Slide 20
Discharge per Unit Width Results
for 50-year Flow (Hilary) – 2019 Topography
5. HYDRAULIC AND SCOUR RE-EVALUATION CONT’D
Discharge per Unit Width Results
for 50-year Flow (Hilary) – Current Conditions (2024 Topo)
P6
P5
P6
P5
P6
P5
P6
P5

## Slide 21
Note: The elevations presented in this plot are referenced to the as-built plans of the original structure built 1952.
The bridge structure is stable based on current conditions of pile exposure at Piers 5 and 6 (Office of Load Ratings)
5. CURRENT CONDITIONS AND NEXT STEPS

## Slide 22
Note: The elevations presented in this plot are referenced to the as-built plans of the original structure built 1952.
The bridge structure is stable based on current conditions of pile exposure at Piers 5 and 6 (Office of Load Ratings)
5. CURRENT CONDITIONS AND NEXT STEPS CONT’D

## Slide 23
5. CURRENT CONDITIONS AND NEXT STEPS CONT’D
Tilt Sensors and Water Level Meter have been installed at both bridges (Completed)
Hydraulic and Scour Re-Evaluation for 25yr, 50-yr, 100-yr and 200-yr (Completed)
Structural Stability Analysis based on predicted scour and bed degradation
performed by Load Ratings Office and Office of Geotechnical Services (Ongoing)
Structure Maintenance Investigation’s Strategy Meeting to discuss mitigation strategies for protecting both structures (Scheduled on 09/05/2024)
Thanks!