## Slide 1
SENSITIVITY OF THEORETICAL SCOUR TO MODELING AND PARAMETERIZATION ALTERNATIVES FOR BRIDGES IN HEC-RAS 2D
August 28, 2024
Shams Al-Amin, PhD, PE, CFM, ENV SP | sal-amin@vhb.com

## Slide 2
Agenda
Fundamentals of HEC-RAS 2D sub-grid bathymetry
Overview of different modeling approaches
Comparison of velocity gradients
Comparison of flow patterns
Comparison of scour
1
2
3
4
5

## Slide 3
HEC-RAS Sub-Grid Bathymetry
“All models are wrong, but some are useful”
Captures the details of the sub grid terrain through hydraulic properties table
Hydraulic properties are developed for each cell & each cell face
Allows for larger computational cells without losing too much of the details of underlying terrain

## Slide 4
1D vs 2D Hydraulic Modeling

## Slide 5: SWE vs DWE
Shallow Water Equation Applications
  Flows with dynamic changes in acceleration
  Wave impacts or tidal influences
  Detailed solutions around obstructions, bridges, or bends
  Coriolis, mixing, or wind influences
  High-resolution and detailed results
Diffusion Wave Applications
  Flow driven mainly by gravity and friction
  No waves or tidal influence
  Approximate flood extent estimate
  Quick estimations or preliminary model runs
Notes: Mass Conservation (Continuity)
Full Momentum Conservation
    Gravity and friction
    Hydrostatic Pressure
    Acceleration (local and convective)
    Turbulent eddy viscosity (optional)
    Wind forces (optional)
    Coriolis term (optional)
Diffusion Wave
    Gravity and friction
    Hydrostatic Pressure

## Slide 6: Bridge Structures inside 2D Flow Areas
SA/2D Connection for bridges in 2D Flow Areas
Headwater-Tailwater Rating Curves
Hydraulics at bridge faces are solved in 2D
Capabilities to model additional hydraulic structures (culverts, gates, weirs, dam breaches)

## Slide 7
Case Study
Wake 61 Bridge Replacement Project, NCDOT
Replacement of an existing NCDOT bridge on SR 1630 (Green Level Church Rd) over Kit Creek in Wake County.
  Bridge concrete deck with concrete on timber caps and piles (3@+/-30’, OAL= 91’)
  Corrugated Metal Box Culvert 16.0’ x 6.1’
  Multiple opening analysis in 1D
Thanks to division 5 and Hydraulics unit, NCDOT

## Slide 8: Setting up the 2D Model
Developing a Terrain Model and Geospatial Layers
Development of the 2D Computational Mesh
Boundary and Initial Conditions for 2D Flow Areas
Running a Model with 2D Flow Areas
Viewing 2D or 1D/2D Output using HEC-RAS Mapper

## Slide 9: Terrain Modification Approach
Piers and abutments added as terrain modifications
No SA/2D connection
Terrain

## Slide 10: SA/2D Approach
Piers and abutments added as terrain modifications
SA/2D connection

## Slide 11: Hybrid Approach
Piers added as terrain modifications
SA/2D connection with abutments

## Slide 12: Comparison of Velocity Maps- 100-yr Event
Terrain Modification
SA/2D
Hybrid

## Slide 13: Comparison of Velocity Maps- 500-yr plus Event
Terrain Modification
SA/2D
Hybrid

## Slide 14: Comparison of Pier Scours
Approach | 100 -yr | 500plus-yr
Terrain Only | 5.1 | 5.9
SA/2D | 4.8 | 5.3
Hybrid | 4.9 | 5.3
Pier Scour Depth (ft)
Reasonably robust when not in pressure and/or weir flow condition
SA/2D more appropriate when in pressure and/or weir flow. Difference may vary based on bridge modeling approach selection.
Reasonably robust in modeling details for SA/2D approach
Notes: Correction factor for pier nose shape K2
Correction factor for angle of attack of flow K3
Correction factor for bed condition K4
Correction factor for armoring of bed material a
Pier width

## Slide 15: Comparison of Contraction Scours
Approach | 100 -yr | 500plus-yr
Terrain Only | 1.9 | 2.7
SA/2D | 2.4 | 2.7
Hybrid | 1.9 | 2.3
Contraction Scour Depth (ft)
Contraction scours are comparable
Pressure flow and live bed scour condition
Difference in stage/flow hydrograph and rating curve between SA/2D approach
Notes: Laursen's (1960) live-bed scour
Average depth in the main channel or floodplain at the approach sectionfeet (meters)y0
Average depth in the main channel or floodplain at the contracted section before scourfeet (meters)Q1
Flow in the main channel or floodplain at the approach section, which is transporting sedimentcfs (m3/s)Q2
Flow in the main channel or floodplain at the contracted section, which is transporting sedimentcfs (m3/s)W1
Bottom width in the main channel or floodplain at the approach section. This is approximated as the top width of the active flow area in HEC-RAS.

## Slide 16
Two-Dimensional Hydraulic Modeling for Highways in the River Environment (FHWA)
HEC-RAS User Manual (USACE)
HEC-RAS Mapper User Manual (USACE)
HEC-RAS Hydraulic Reference Manual (USACE)
Available Guidance Materials
1
2
3
4
Notes: https://www.fhwa.dot.gov/engineering/hydraulics/pubs/hif19061.pdf
https://www.hec.usace.army.mil/confluence/rasdocs/rasum/latest
https://www.hec.usace.army.mil/confluence/rasdocs/rmum/latest

## Slide 17: Thank you!
Shams Al-Amin, PhD, PE, CFM, ENV SP | sal-amin@vhb.com