## Slide 1: Selection and Application of Manning’s Roughness Values in Two-Dimensional Hydraulic Models: Results from NCHRP 24-49
Ali Mahdavi Mazdeh, Ph.D., Lyle Zevenbergen, P.E. Casey Kramer, P.E. and Xiaofeng Liu, Ph.D., P.E.

## Slide 2: What is Manning’s n?
Uniform flow and flow resistance
Robert Manning
1816-1897
Image: wikipedia

## Slide 3: Is the problem solved?
Lots of confusion and misconceptions on Manning’s n
Manning’s n the same in 1D and 2D models?
Manning’s n the same in different 2D models?
How does HEC-RAS subgrid terrain affect Manning’s n?
How does turbulence model affect Manning’s n?
…

## Slide 4: What is Manning’s n?
Lack of clear definitions of Manning’s n in different contexts
  In physical world
  In numerical modeling world

## Slide 5: What is Manning’s n?
In physical world:
  Manning’s n is a parameter to quantify flow resistance induced by different factors, such as grain roughness, bedforms, vegetation, channel irregularity, etc.
Total flow resistance:

## Slide 6: What is Manning’s n?
In physical world:
  How to get the (total) Manning’s n?
    Tabular method
    Photographic method
    Quantitative method
USGS online photo guide for Manning’s n

## Slide 7: What is Manning’s n?
In numerical modeling world:
  Models such as SRH-2D and HEC-RAS 2D solve 2D shallow water equations
Can we directly use Manning’s n
from textbook?

## Slide 8: What is Manning’s n?
In numerical modeling world:
  Part of flow resistance factors are resolved by terrain and mesh

## Slide 9: What is Manning’s n?
In numerical modeling world:
  Part of flow resistance factors are resolved by terrain and mesh
  The rest is unresolved  specified in 2D models!

## Slide 10: What is Manning’s n?
In numerical modeling world:
  Total flow resistance = Resolved flow resistance + Unresolved flow resistance
is a physical AND numerical parameter!

## Slide 11: What is Manning’s n?
In numerical modeling world:
  nunresolved is what needs to be specified in 2D models
  nunresolved depends on many factors:
    Terrain and mesh resolutions
    Whether key hydraulic controls are captured
    Model’s numerical schemes
    Subgrid terrain treatment
    Turbulence models
    …

## Slide 12: How to get unresolved Manning’s n?
Terrain/mesh resolution vs. resolved/unresolved Manning’s n
Working hypothesis

## Slide 13: How to get unresolved Manning’s n?
“Quarter-circle” method
Details in NCHRP 24-49 Project Report

## Slide 14: How to get unresolved Manning’s n?
“Quarter-circle” method
Details in NCHRP 24-49 Project Report

## Slide 15: How to get unresolved Manning’s n?
For each roughness zone, determine resolved vs. unresolved Manning’s n
  For low to moderate resolution terrain and mesh:
  For medium resolution terrain and mesh:
  For high resolution terrain and mesh:
Details in NCHRP 24-49 Project Report

## Slide 16: More specific questions
Manning’s n in 1D vs. 2D models?
Effect of HEC-RAS 2D’s subgrid terrain treatment?
Same Manning’s n in SRH-2D and HEC-RAS 2D?
Importance of Manning’s n for different flow profiles?
Manning’s n used for sediment transport?
…

## Slide 17: More specific questions
Should we reduce Manning’s n when transitioning from 1D to 2D?
Answer: Not necessarily.
Reason: There are other parameters in 1D such as contraction/expansion coefficients.

## Slide 18: More specific questions
Does HEC-RAS 2D’s subgrid terrain treatment reduce Manning’s n?
Answer: Likely, but not definitely.
Reason(s): Slope (gravity) term does not use subgrid terrain.

## Slide 19: More specific questions
Same Manning’s n in SRH-2D and RAS 2D?
Answer: No.
Reason(s): Modeling approach differences in subgrid terrain treatment, turb. models, numerical schemes, etc.

## Slide 20: More specific questions
How important is Manning’s n anyway?
Answer: Depends on flow profiles and domain length.
Reason(s): Manning’s n is
  less important in deeper water than in shallow water depth.
  less important in short distance.

## Slide 21: Manning’s n: A good 2D model is key
Best practices for 2D hydraulic modeling
Details in NCHRP 24-49 Project Report

## Slide 22: Manning’s n guidelines
A decision-making process
Details in NCHRP 24-49 Project Report

## Slide 23: Further details
X. Liu, A., Mazdeh, L. W., Zevenbergen, and C. M., Kramer (2024). Selection and Application of Manning's Roughness Values in Two-Dimensional Hydraulic Models. NCHRP Research Report 1077
https://www.trb.org/Publications/Blurbs/183186.aspx

## Slide 24: Take-home message
Manning’s n specified in 2D models should be nunresolved
“Quarter-circle method”
“Roulette method”
or

## Slide 25: More specific questions
In physical world
In numerical models