## Slide 1: FHWA Metric #18, National Bridge Inspection Standards
Roundtable Discussion
28 August 2024
Notes: As we begin this roundtable discussion, we don’t intend this to be another presentation (although my portion may feel like it).
I thought it would be helpful to briefly describe where this FHWA 23 Metric review approach came from, where its regulatory basis resides and what is included in the process.
Then we will let the other panelists discuss their involvement in the process and hopefully provide the audience with potential solutions to address any deficiencies within your State’s Scour program.

## Slide 2: DISCLAIMER
Except for the statutes and regulations cited, the contents of this document do not have the force and effect of law and are not meant to bind the States or the public in any way. This document is intended only to provide information regarding existing requirements under the law or agency policies.
The U.S. Government does not endorse products or manufacturers. Trademarks or manufacturers’ names appear in this presentation only because they are considered essential to the objective of the presentation. They are included for informational purposes only and are not intended to reflect a preference, approval, or endorsement of any one product or entity.
The Federal Highway Administration (FHWA) does not endorse any entity and the appearance of our presentation material in this template should not be interpreted as an endorsement or statement exhibiting any preference, support, etc.
Unless otherwise noted, FHWA is the source of all images in this product/ presentation.

## Slide 3: FHWA’s 23 Metrics Process
23 metrics traced directly to the NBIS regulations
Nationwide implementation - February 2011
Division Bridge Engineer assesses each metric at ‘minimal level’ each year, and over a 5-year cycle, each metric is assessed at ‘intermediate level’ or ‘in-depth level’
Notes: - In 2010, in response to a recommendation from the Office of the Inspector General (OIG) and Congressional direction, the FHWA developed a new systematic, data-driven, and risk-based oversight process for monitoring State compliance with the National Bridge Inspection Standards (NBIS).

## Slide 4: FHWA’s Risk-based and Data-driven Process
23 metrics – risk-based and data-driven process agencywide
  Ensures each State is held to the same standard for compliance
  Allows States and FHWA to track trends and assess resources to improve deficiencies
Risk Factors associate with the 23 Metrics:
  The use of ‘sampling’
  The use of ‘substantial compliance’
Notes: The risk-based and data-driven process was primarily targeting:
- a National standard of compliance with the NBIS
- allow owners to better manage their resources
The risk factors associated with the 23 metrics are
- the use of sampling to select bridges to assess an Owner’s bridge inventory (ability to make inferences about the entire bridge inventory)
- the use of ‘substantial compliance’ status to accept minor deficiencies within each metric with the understanding that the owner will develop an Improvement Plan to mitigate the risk with those minor deficiences

## Slide 5: Metric 18 (Scour) Risk Factors
Risk-based and data-driven Scour Appraisals
Risk-based and data-driven Plans of Action
Notes: Risk-based scour appraisals allow the use of HEC-20 Scour Assessments for low-risk bridges needing an appraisal and HEC-18 Scour Evaluations for high-risk bridges.
Risk-based Plans of Action allow the use of low/medium/high risk POAs that are commensurate with State’s defined risk. The countermeasures can also be risk-based where physical countermeasures are expected for high-risk bridges and a monitoring countermeasure may be appropriate for low-risk bridges
There are other risk-based design considerations in HEC-18

## Slide 6: NBIS Scour Regulations – 23 CFR 650.313(o)
(o) Scour.
  (1) Perform a scour appraisal for all bridges over water, and document the process and results in the bridge file. Re-appraise when necessary to reflect changing scour conditions. Scour appraisal procedures should be consistent with Hydraulic Engineering Circulars (HEC) 18 and 20. Guidance for scour evaluations is located in HEC 18 and 20, and guidance for scour assessment is located in HEC 20
  (2) For bridges which are determined to be scour critical or have unknown foundations, prepare and document a scour POA for deployment of scour countermeasures for known and potential deficiencies, and to address safety concerns. The plan must address a schedule for repairing or installing physical and/or hydraulic scour countermeasures, and/or the use of monitoring as a scour countermeasure. Scour plans of actions should be consistent with HEC 18 and 23
  (3) Execute action in accordance with the plan
Notes: I mentioned earlier that each metric is traced to the regulations. Metric 18 is tied to .313(o)(1), (2), and (3).
Requires an Appraisal for all bridges over water. (I will define Appraisal on the next slide)
  Re-appraise when conditions change from the original appraisal. **Likely includes you as a hydraulic engineer.
  There is a good chance that many of your State’s bridge records include the scour evaluations performed in the late 1990s to early 2000s. These evaluations were not intended to be a one-n-done evaluation.
  There is a chance that site conditions have changed over the years. State Hydraulic engineers, NBIS Program managers and a multidisciplinary team should begin internal discussions to ask, ‘Do the old scour evaluations appropriately reflect current conditions and vulnerability determinations?’
(2) Requires a Plan of Action for Scour Critical bridge and bridges with Unknown Foundations. ** Development may include you as a hydraulic engineer
(3) Implement the POA when triggering event occurs

## Slide 7: Risk-Based, Data Driven Scour Program
April 9, 2012 memo, applying risk to the Scour Program
  Scour evaluation element
    Scour evaluation vs. Scour assessment
  Scour critical element
  Unknown foundation element
  Developing POAs
  Owners may programmatically adopt a risk-based scour program
    Should consider ‘Likelihood’ and ‘Consequence of failure’
Notes: Same risk-based guidance document addresses ‘scour critical’ element, ‘UF’ element, and POAs
Owners should update their program manual to include criteria that defines ‘high risk’ vs ‘low risk’ structures to avoid ‘cherry picking’ the application of risk-based measures
The AASHTO Manual for Bridge Evaluation also discusses the need to perform scour evaluations

## Slide 8: Scour Appraisal
Scour appraisal. A risk-based and data-driven determination of a bridge's vulnerability to scour, resulting from the least stable result of scour that is either observed, or estimated through a scour evaluation or a scour assessment.
  Scour evaluation. The application of hydraulic analysis to estimate scour depths and determine bridge and substructure stability considering potential scour (HEC-18/20).
  Scour assessment. The determination of an existing bridge's vulnerability to scour which considers stream stability and scour potential (HEC-20).
Notes: These definitions are taken from the NBIS regulations
This Scour Appraisal term is probably new to many of you

## Slide 9: Plans of Action (POAs)
Scour plan of action (POA). Procedures for bridge inspectors and engineers in managing each bridge determined to be scour critical or that has unknown foundation
2 primary components:
  instructions regarding the type and frequency of inspections to be made at the bridge while monitoring the bridge
  schedule for the timely design and construction of scour countermeasures
Notes: POA is defined in the NBIS regulations and described in HEC-18 and 23
Speaking of risk-based, the premise of leaving the risk associated with a scour critical bridge in service is that the owner will mitigate that risk with the steps within the POA.

## Slide 10: Metric 18 Criteria
Notes: The DBEs will be assessing 2 populations of bridges that are evaluated for compliance with NBIS:
- Bridges over water – reviewing files to verify scour appraisals are documented and relevant
- Bridge that are scour critical or have unknown foundations – verify that POAs are documented and being implemented

## Slide 11: Metric 18 Compliance
- Compliance
- Substantial Compliance (requires an ‘Improvement Plan’)
- Non-Compliance (requires a ‘Plan of Corrective Action’)
Notes: Annually, the DBE will make a compliance determination for each of the 23 Metrics

## Slide 12
Paul Sharp (paul.sharp@dot.gov)
FHWA Senior Scour Engineer

## Slide 13: FHWA Division Bridge Engineer
Ed Miltner - Idaho
The role and processes of Division Bridge Engineers in Metric 18.
Notes: Annually, the DBE will make a compliance determination for each of the 23 Metrics

## Slide 14: State Hydraulic Engineers
Herb McDowell – Idaho Transportation Department
Monte Deis - North Dakota DOT
The State DOT perspective in Metric 18

## Slide 15: Ayres Associates
Will DeRosset - Hydraulic Engineer
A consultant’s role in helping States navigate this process.

## Slide 16: M18 - Substantial Compliance Determination

## Slide 17: Low Risk POA